## Slide 1: Collaborative work for Hi-ASAP
12 Oct 2021
1
Topic: Characterization of fine particulate matter (PM1.0 and PM2.5) from incense burning in temples in Asian countries
To Thi Hien et al.
Faculty of Environment, University of Science, Vietnam National University, Ho Chi Minh City

## Slide 2: Background
2
- Incense stick burning is one of common and popular ritual in East and Southeast Asian countries, including Vietnam
Incense burning generates many gaseous and particulate pollutants, especially fine particles (PM1.0, PM2.5)
 It is important to study fine particles emitted from incense burning and personal exposure to PM

## Slide 3: Objectives
3
To assess and compare concentration levels of fine particles from incense burning in the temples (PM1.0 and PM2.5) in Asian countries
Calculating exposure to PM1 and PM2.5 from incense burning
If possible: OC/EC

## Slide 4: Methods
4
Measure PM1.0 and PM2.5 in temples using low-cost sensors
Collect PM2.5 for determine OC/EC
Instrument: AS-LUNG or other sensors (sensors need to be calibrated)
Site: 1 - 2 temples in the city
Timeline: monitor PM twice per month:
    The 1st and the full moon day (15th) of lunar month
    2 days before and 2 days after the 1st and the 15th of lunar month
    4 hours in the morning (7:30 – 11:30)
    4 hours in the afternoon (13:45 – 17:45)

## Slide 5
Monitor PM by sensor (AS-LUNG is the best):
  Mobile: Research staff will carry AS-LUNG in front of their chest or on their shoulder and move around the temple for 4 hours, and count number of incense stick per 30 min (average 1 stick will burn during 30 min)
  Fixed: measure the concentration of PM outside at the temple gate next to street where there are traffic activity, and count number of worshipper every 1 hour
  Resolution: 1 min
Sampling PM2.5 by impactor sampler to analysis OCEC
  Fixed: using impact sampler (quartz filter) to collect PM2.5 during 4 hours in the morning and in the afternoon
5

## Slide 6
Temple 1
Temple 2
Impact Sampler
Worshipper
6

## Slide 7: Some initial results…
Temple 1
Temple 2
Research staff was standing near the incensory
7

## Slide 8: PM1, PM2.5 on full moon day (15th)/1st of lunar month and on 2 days before and after
9

## Slide 9
9
Thank you for your attention!