## Slide 1: Health Investigation and Air Sensing for Asian Pollution (Hi-ASAP)
SC Candice Lung, WC Vincent Wang
Research Center for Environmental Changes, Academia Sinica

## Slide 2: Proposed topic 1: Field and laboratory evaluations of low-cost sensors in the Asian cities with different emission sources (authors: WC Vincent Wang, SC Candice Lung‬, and other interested collaborators)
Background:
  Environmental PM2.5 level is a common but serious issue in Asian cities. A suitable PM2.5 sensing device can help to monitor PM2.5 levels from various emission sources in the Asian cities.
Objective:
  To evaluate the performance of AS-LUNG sets by conducting side-by-side comparison with research-grade instruments in laboratory, indoor, and ambient environments.
Table. 1 Comparison data upload format
 | Item |  | Item
1. | country | 10. | sensing device
2. | region/area | 11. | sensing device_sensor
3. | longitude | 12. | sensing device_sensorPM1
4. | latitude | 13. | sensing device_sensorPM2.5
5. | comparison environment | 14. | reference instrument
6. | comparison environment description | 15. | reference instrument_PM1
7. | main emission sources | 16. | reference instrument_PM2.5
8. | UTC (coordinated universal time) | 17. | temperature
9. | season | 18. | relative humidity
Note: You may start to conduct side-by-by comparison now; we only need 7 days of monitoring data for each city
Data collection:
  All Hi-ASAP members are welcome to join this topic and upload your own PM2.5 comparison data.
  These PM2.5 data should be monitored on non-rainy days.
  Please email the data file to:
  phdzen@gate.sinica.edu.tw
Fig. 1 Side-by-side PM2.5 comparison in the enclosed chamber (Wang et al., 2020, Sensor)

## Slide 3: Environment of side-by-side comparison
Hood
Chamber
Roof
Indoor
Outdoor

## Slide 4: Data collection
Country | City | Environment | Emission | Data intervals(min) | Reference instrument
Taiwan | Taipei | outdoor | ambient | 1 | GRIMM
Taiwan | Taipei | chamber | incense | 1 | GRIMM
Bangladesh | Dhaka | indoor | ambient | 15 | BlueSky Air Quality Monitor
Vietnam | Ho Chi Minh | chamber | incense | 1 | DustTrak
Myanmar | Mandalay | outdoor | waste burning | 1 | EPAS

## Slide 5: Thank you for your attention!